## Slide 1: P4 Programmable Data Plane Switches
Joseph Telaak, Elie Kfoury, Jose Gomez, Ali AlSabeh, Shararin Sharif, Jorge Crichigno, PhD.

## Slide 2: Traditional Switching
Hubs
  Layer 1 (Physical)
  Forwards everything everywhere
    Relies on packet dropping
  Slow
    Can cause DOS on large networks
Unmanaged switches
  (Layer 2 Data-Link)
  Forwards based on MAC
  Popular to just add more ports
Managed Switches
  Layer 2 with Layer 3 (Network) functionality
  Operates very similarly to unmanaged
    Has added configurability & security
    Can do some routing (VLANs)
    Modify control plane but not data plane
  Best for buildings and datacenters

## Slide 3: Control & Data Plane
Control Plane
  Defines logic to determine how packets are switched by the data plane
    Independent of Data Plane
  Contains routing table
  Applications like QoS
  Protocols like BGP, OSPF, IS-IS
Data Plane
  Functions & Processes for packet switching
  Parser & De-parser
E. F. Kfoury, J. Crichigno and E. Bou-Harb, "An Exhaustive Survey on P4 Programmable Data Plane Switches: Taxonomy, Applications, Challenges, and Future Trends," in IEEE Access, vol. 9, pp. 87094-87155, 2021, doi: 10.1109/ACCESS.2021.3086704.

## Slide 4: P4
(Programming Protocol-Independent Packet Processors)
Programming language developed in 2014
  Target-Independent (CPU & ASICs)
    ASICs are significantly faster
No native protocol support
  Everything defined by programmer
Allows researchers to develop protocols faster
  Feature rollout from vendors takes years
E. F. Kfoury, J. Crichigno and E. Bou-Harb, "An Exhaustive Survey on P4 Programmable Data Plane Switches: Taxonomy, Applications, Challenges, and Future Trends," in IEEE Access, vol. 9, pp. 87094-87155, 2021, doi: 10.1109/ACCESS.2021.3086704.

## Slide 5: Applications
In-Band Network Telemetry
  Add metadata in transit
  Adjust sending rates to reduce congestion
Load Balancing
  Do forwarding on the switch and manage table on a server
    Instead of forwarding from the server
Machine Learning
  Aggregate data on switch instead of on workers (Aggregation is cheap)
E. F. Kfoury, J. Crichigno and E. Bou-Harb, "An Exhaustive Survey on P4 Programmable Data Plane Switches: Taxonomy, Applications, Challenges, and Future Trends," in IEEE Access, vol. 9, pp. 87094-87155, 2021, doi: 10.1109/ACCESS.2021.3086704.